## Slide 1
A STUDY NOTEBOOK IN DIGITAL SIGNAL PROCESSING
Radix-2 Decimation-in-Time (DIT) FFT
From the DFT Equation to an 8-Point FFT
Xk = Ek + WNk Ok the radix-2 DIT decomposition
Derivation · Twiddle Factors · Butterfly · Bit-Reversal · Worked 8-Point Example · Hardware Mapping
Reference document for MATLAB, FPGA, and RTL implementation

## Slide 2
SECTION 1 · ROADMAP
Learning Objectives
After studying this deck, you should be able to explain, derive, and calculate every part of a radix-2 DIT FFT, not just recognize the final diagram.
✓
The difference between the DFT and the FFT
✓
Why the FFT is computationally efficient (O(N log2 N) vs O(N^2))
✓
What “radix-2” means and why N must be a power of 2
✓
What “decimation-in-time” means
✓
How the DFT summation is decomposed into even and odd terms
✓
Full derivation of the radix-2 DIT equations
✓
The origin and meaning of twiddle factors W_N^k
✓
How the butterfly operation falls directly out of the algebra
✓
How the algorithm organizes into log2(N) FFT stages
✓
Why bit-reversed input ordering is required
✓
A complete, hand-checked 8-point FFT calculation
✓
How the math maps to the flow graph, operation counts, and hardware / DSP implementation
Radix-2 Decimation-in-Time FFT
Introduction
2

## Slide 3
SECTION 2 · START FROM THE DFT
The N-Point Discrete Fourier Transform
Xk = Σn=0N-1 xn WNnk
WN = e-j2π/N
W_N is called the twiddle factor: a complex number of magnitude 1 that rotates a phasor by angle 2π/N in the clockwise (negative) direction. Each term x[n]·W_N^(nk) is a single complex multiply-add.
Symbol | Meaning
x[n] | The n-th sample of the input signal in the time domain, n = 0, 1, ..., N-1
X[k] | The k-th sample of the output spectrum in the frequency domain, k = 0, 1, ..., N-1
N | The transform length: the number of time samples and the number of frequency bins
n | Time index. Runs over every input sample for every output X[k]
k | Frequency-bin index. Selects which frequency component is being measured
W_N | The twiddle factor e^(-j2π/N): a unit-magnitude complex rotation
e^(-jθ) | Complex exponential: cos(θ) - j sin(θ), a point on the unit circle
Radix-2 Decimation-in-Time FFT
The DFT
3

## Slide 4
SECTION 2 · START FROM THE DFT
Sine / Cosine Form, and Where the Cost Comes From
Trigonometric (rectangular) form of the twiddle factor
WNk = cos(2πk/N) − j sin(2πk/N)
Every complex exponential is just a cosine (real part) and a negative sine (imaginary part). Computing X[k] therefore always means real multiply-accumulates on both the real and imaginary parts, not a single abstract operation.
Where the O(N²) cost comes from
Each output X[k] is a sum over all N input samples: N complex multiply-accumulate (MAC) operations.
There are N such outputs, k = 0 ... N-1.
Total work = N outputs × N terms per output = N² complex MACs.
No structure in the sum is being reused: every W_N^(nk) is treated as an independent number.
Concrete case, N = 8: computing X[0] alone needs 8 complex multiply-adds (one per n). Computing all 8 outputs, X[0] through X[7], needs 8 × 8 = 64 complex multiply-accumulate operations.
This is the direct-computation cost. Nothing here is wrong, it is simply brute force: every one of the N² products W_N^(nk) is computed and used once, even though many of them are related to each other by simple symmetry (Section 8). The FFT exploits exactly that redundancy.
N (outputs) | Terms per output | Total complex MACs | Order
4 | 4 | 16 | O(N²)
8 | 8 | 64 | O(N²)
16 | 16 | 256 | O(N²)
1024 | 1024 | 1,048,576 | O(N²)
Radix-2 Decimation-in-Time FFT
The DFT
4

## Slide 5
SECTION 3 · WHY FFT?
Same Transform, a Far More Efficient Algorithm
Key idea: the FFT does not compute a different transform from the DFT. It computes exactly the same X[k] values. The FFT is an algorithm for evaluating the DFT summation with far fewer arithmetic operations, by reusing partial results instead of recomputing them for every output.
 | Direct DFT | Radix-2 FFT
Result computed | X[k], k = 0..N-1 | X[k], k = 0..N-1 (identical values)
Strategy | Evaluate the full sum for every k independently | Recursively split the sum, reuse smaller results
Complex multiplications | O(N²) | O(N log₂N)
Growth as N doubles | Roughly quadruples | Roughly just-over-doubles
N = 8 in numbers
Direct DFT: 82 = 64 operations
Radix-2 FFT: 8×log28 = 8×3 = 24 op.
The 24 counts here are butterfly-equivalent operations (N log2 N); Section 14 derives the exact count of 12 butterflies, each containing one multiply and two adds, for N = 8. The FFT wins because each butterfly output is reused as an input to the next stage instead of being one disposable term inside a giant independent sum.
Radix-2 Decimation-in-Time FFT
Why FFT
5

## Slide 6
SECTION 4 · RADIX-2
What Does “Radix-2” Mean?
“Radix” is the base of a decomposition, the number of pieces a problem is split into at each step.
Radix-2 means: at every step, split one DFT into two half-size DFTs.
Each half-size DFT is cheaper than the original, and two of them together still cover every input sample exactly once.
Applying the split repeatedly turns one large, expensive DFT into many tiny, cheap DFTs plus some recombination arithmetic (the butterfly).
8 → 4 + 4 → 2+2+2+2 → 1+1+1+1+1+1+1+1
Recursive decomposition for N = 8
8-point FFT
4-point FFT
4-point FFT
2-point
2-point
2-point
2-point
8 single input samples: x[0] ... x[7], each trivially its own 1-point DFT
Why N must be a power of 2: radix-2 works by repeatedly halving N. That only produces a clean recursion down to trivial 1-point transforms if N, N/2, N/4, ... eventually reaches 1 with no remainder. This requires N = 2^m for an integer m. If N is not a power of 2, radix-2 cannot split evenly, and a different radix (e.g. radix-3, radix-4) or a mixed-radix / Bluestein algorithm is required instead.
Radix-2 Decimation-in-Time FFT
Radix-2
6

## Slide 7
SECTION 5 · DECIMATION-IN-TIME
Splitting the Input by Time-Index Parity
“Decimation” here does not mean discarding samples. It means splitting the input sequence into two interleaved subsequences based on whether the time index n is even or odd, and processing each half separately.
Original 8-point input sequence, in natural order
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
Even-indexed samples (teal)
x[0]
x[2]
x[4]
x[6]
Odd-indexed samples (amber)
x[1]
x[3]
x[5]
x[7]
DIT operates by decomposing the input sequence itself. Even samples x[0], x[2], x[4], x[6] feed one N/2-point DFT; odd samples x[1], x[3], x[5], x[7] feed a second N/2-point DFT. The two N/2-point results are then recombined with the butterfly (Sections 6 and 7) to form the final N-point spectrum. The split happens on the time-domain input, which is exactly why it is called decimation-in-time.
Radix-2 Decimation-in-Time FFT
Decimation-in-Time
7

## Slide 8
SECTION 5 · DECIMATION-IN-TIME
DIT vs. DIF at a Glance
Decimation-in-time (DIT) is not the only way to recursively split the DFT. Decimation-in-frequency (DIF) is the dual approach: instead of splitting the input samples, it splits the output frequency bins. Both compute the identical DFT; the deck focuses on DIT.
Feature | Decimation-in-Time (DIT) | Decimation-in-Frequency (DIF)
What is split | The time-domain input sequence, by index parity | The frequency-domain output, by index parity
Input ordering | Bit-reversed | Natural
Output ordering | Natural | Bit-reversed
First operation | Combine small DFTs (decompose then combine) | Butterfly first, then decompose smaller DFTs
Twiddle multiply | Applied to O[k] before the add / subtract | Applied after the add / subtract
Typical interpretation | “Split input samples, then combine” | “Split frequency outputs, then recurse”
Both algorithms produce exactly the same X[k]. They differ only in how the computation is organized internally: which domain is decimated, and consequently where the bit-reversal shuffle ends up (input side for DIT, output side for DIF).
Radix-2 Decimation-in-Time FFT
DIT vs DIF
8

## Slide 9
SECTION 6 · DERIVATION
Step 1: Split the DFT Sum by Index Parity
Xk = Σn=0N-1 xn WNnk
Every index n from 0 to N-1 is either even (n = 2r) or odd (n = 2r+1), for r = 0, 1, ..., N/2 - 1. Splitting the single sum into these two groups changes nothing mathematically, it only regroups the same N terms:
Xk = Σr=0N/2-1 x2r WN2rk + Σr=0N/2-1 x2r+1 WN(2r+1)k
The first sum (teal) runs over the even samples x[0], x[2], x[4], ..., x[N-2], substituting n = 2r.
The second sum (amber) runs over the odd samples x[1], x[3], x[5], ..., x[N-1], substituting n = 2r+1.
Each sum now has only N/2 terms instead of N, but there are two of them, so the total number of terms is unchanged, 2 × N/2 = N. Nothing has been saved yet; the next steps show where the saving actually comes from.
Radix-2 Decimation-in-Time FFT
Derivation
9

## Slide 10
SECTION 6 · DERIVATION
Step 2: Simplify the Twiddle Exponents
Even-term exponent
WN2rk = ( e-j2π/N )2rk = e-j2πrk/(N/2) = WN/2rk
The factor of 2 in the exponent cancels the factor of 2 hiding inside W_N (since W_N = e^(-j2π/N)). The result, W_N/2^(rk), is simply the twiddle factor of a DFT that is half as long. This is the algebraic heart of the whole method: an N-point twiddle factor collapses into an N/2-point twiddle factor.
Odd-term exponent
WN(2r+1)k = WN2rk · WNk = WNk WN/2rk
The exponent (2r+1)k splits into 2rk + k using exponent rules for W_N^a·W_N^b = W_N^(a+b). The 2rk part reduces exactly as in the even case to W_N/2^(rk). What is left over is a single extra factor, W_N^k, that does not depend on r. This leftover factor is the twiddle factor: it is pulled outside the odd summation in Step 3.
Radix-2 Decimation-in-Time FFT
Derivation
10

## Slide 11
SECTION 6 · DERIVATION
Step 3: Define E[k] and O[k], Then Combine
Substituting the simplified exponents back into the two sums from Step 1 gives:
Xk = Σr=0N/2-1 x2r WN/2rk + WNk Σr=0N/2-1 x2r+1 WN/2rk
Notice that both remaining sums are themselves N/2-point DFTs: one of the even samples, one of the odd samples, both using the smaller twiddle factor W_N/2. Give each one a name:
Ek = Σr=0N/2-1 x2r WN/2rk
Ok = Σr=0N/2-1 x2r+1 WN/2rk
E[k] is the N/2-point DFT of the even samples. O[k] is the N/2-point DFT of the odd samples. Substituting these definitions back gives the central result of the radix-2 DIT derivation:
Xk = Ek + WNk Ok
Valid for k = 0, 1, ..., N/2 - 1 as written; the next slide extends it to the full range k = 0, ..., N-1.
Radix-2 Decimation-in-Time FFT
Derivation
11

## Slide 12
SECTION 6 · DERIVATION
Step 4: Extending to the Full Range With Periodicity
E[k] and O[k] are each N/2-point DFTs, so both are periodic with period N/2: E[k + N/2] = E[k] and O[k + N/2] = O[k]. This periodicity is what lets one formula generate the second half of the outputs for free.
Evaluate X[k] at k + N/2:
Xk+N/2 = Ek+N/2 + WNk+N/2 Ok+N/2 = Ek + WNk+N/2 Ok
Now use the twiddle-factor half-period symmetry (derived in full in Section 8): W_N^(k+N/2) = −W_N^k. This flips the sign of the twiddle term only:
Xk+N/2 = Ek − WNk Ok
This is the payoff of the whole derivation. The same two numbers, E[k] and W_N^k O[k], produce both X[k] and X[k+N/2]: one add, one subtract, no extra DFT terms. E[k] and O[k] each only need to be computed once for k = 0 ... N/2 - 1, and they are reused to generate the entire N-point output. This reuse, not any single trick, is the source of the FFT's speed.
Radix-2 Decimation-in-Time FFT
Derivation
12

## Slide 13
SECTION 7 · THE BUTTERFLY
The Butterfly Is Not Drawn, It Is Derived
Start from the two results of Section 6:
Xk = Ek + WNk Ok
Xk+N/2 = Ek − WNk Ok
Give the two quantities that actually get combined their own names, A and B:
A = Ek
B = WNk Ok
B is the odd-branch value after it has been rotated by the twiddle factor. With A and B defined, the pair of equations collapses to the simplest possible form:
Xtop = A + B
Xbottom = A − B
This add/subtract pair, with exactly one complex multiplication (forming B) feeding it, is the butterfly. It is called that because of the crossing shape its signal-flow diagram makes, not because it is a separate idea from the algebra above: it IS the algebra above, drawn instead of written.
Radix-2 Decimation-in-Time FFT
The Butterfly
13

## Slide 14
SECTION 7 · THE BUTTERFLY
The Radix-2 DIT Butterfly Flow Graph
E[k] = A
O[k]
⊗
WNk
B = Wₙᵏ O[k]
+
−
X[k]
X[k+N/2]
solid line = added directly (A or B path into its natural output) dashed line = crossed path (the other operand)
Twiddle multiplication happens once, before the add/subtract, on the odd branch only. This is the standard radix-2 DIT butterfly: two complex inputs, one complex multiply, one complex add, one complex subtract, two complex outputs. Every wire in this diagram corresponds to a named term in the equations on the previous slide.
Radix-2 Decimation-in-Time FFT
The Butterfly
14

## Slide 15
SECTION 8 · TWIDDLE FACTORS
Twiddle Factors: Definition and General Form
WNk = e-j2πk/N = cos(2πk/N) − j sin(2πk/N)
W_N^k is always a point on the unit circle in the complex plane: it has magnitude 1 and only changes phase.
As k increases by 1, the phase rotates clockwise by an additional 2π/N radians (360°/N).
Multiplying a complex number by W_N^k therefore rotates it, it never changes its magnitude.
First few powers
Power | Value
W_N^0 | 1 (angle 0°)
W_N^1 | e^(-j2π/N) (angle -360°/N)
W_N^2 | e^(-j4π/N) (angle -720°/N)
Geometric picture: the N values W_N^0, W_N^1, ..., W_N^(N-1) are the N-th roots of unity, N equally spaced points around the unit circle, spaced 360°/N apart, starting at angle 0° and rotating clockwise. For N = 8 they land every 45°.
Radix-2 Decimation-in-Time FFT
Twiddle Factors
15

## Slide 16
SECTION 8 · TWIDDLE FACTORS
Twiddle Factor Values for N = 8
k | Angle | W₈ᵏ = cos − j sin | Rectangular value
0 | 0° | cos0 − j sin0 | 1 + j0
1 | 45° | cos45 − j sin45 | 0.7071 − j0.7071
2 | 90° | cos90 − j sin90 | 0 − j1 = −j
3 | 135° | cos135 − j sin135 | −0.7071 − j0.7071
4 | 180° | cos180 − j sin180 | −1 + j0
5 | 225° | cos225 − j sin225 | −0.7071 + j0.7071
6 | 270° | cos270 − j sin270 | 0 + j1 = j
7 | 315° | cos315 − j sin315 | 0.7071 + j0.7071
k=0
k=1
k=2
k=3
k=4
k=5
k=6
k=7
The 8th roots of unity, spaced 45° apart
Four of these eight values, W8^0=1, W8^2=−j, W8^4=−1, W8^6=j, are trivial: multiplying by them needs no real multiplier, only a sign flip and/or a swap of real and imaginary parts. This matters directly for the operation count in Section 14.
Radix-2 Decimation-in-Time FFT
Twiddle Factors
16

## Slide 17
SECTION 8 · TWIDDLE FACTORS
Symmetries That Make the FFT (and Hardware) Efficient
WNk+N = WNk
Periodicity
Rotating by a full N steps returns to the same point on the unit circle. Twiddle-factor tables only ever need N distinct entries, however large the exponent gets.
WNk+N/2 = −WNk
Half-period (used in Section 6)
A rotation of half the circle is exactly a sign flip. This is precisely what turns X[k+N/2] into A − B instead of a brand-new computation.
WN-k = WNk*
Conjugate symmetry
Negative-frequency twiddle values are just conjugates of positive ones, so only half the unit circle needs to be stored; the rest is a sign flip on the imaginary part.
Radix-2 Decimation-in-Time FFT
Twiddle Factors
17

## Slide 18
SECTION 9 · BUILDING THE 8-POINT FFT
Apply the Decomposition to N = 8
The 8-point input sequence, in natural time order:
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
↓ split by parity, per Section 5 / 6
Even branch, feeds a 4-point DFT called E[k]
x[0]
x[2]
x[4]
x[6]
Odd branch, feeds a 4-point DFT called O[k]
x[1]
x[3]
x[5]
x[7]
Each 4-point DFT is itself a smaller instance of the same problem. E[k] is the 4-point DFT of {x[0], x[2], x[4], x[6]}. O[k] is the 4-point DFT of {x[1], x[3], x[5], x[7]}. Radix-2 says: do not compute either 4-point DFT directly, split each one again by parity, exactly as in Section 6, but now with N replaced by 4. The next slide carries this out fully.
Radix-2 Decimation-in-Time FFT
Building the 8-Point FFT
18

## Slide 19
SECTION 9 · BUILDING THE 8-POINT FFT
Full Recursive Decomposition Down to 2-Point Groups
x[0..7] (8-pt)
x[0],x[2],x[4],x[6] (4-pt E)
x[1],x[3],x[5],x[7] (4-pt O)
x[0],x[4] (2-pt)
x[2],x[6] (2-pt)
x[1],x[5] (2-pt)
x[3],x[7] (2-pt)
x[0]
x[4]
x[2]
x[6]
x[1]
x[5]
x[3]
x[7]
Each 2-point group is a trivial 2-point DFT: DFT2{a,b} = [a+b, a−b], no twiddle multiplication needed (W_2^0 = 1). This is the recursion's base case.
Read this tree from the bottom up, not the top down. Computation actually starts at the leaves: the eight trivial 1-point “DFTs” (a single sample equals its own transform). Adjacent leaves combine into 2-point DFTs using the butterfly with W_2^0=1. Pairs of 2-point results combine into 4-point DFTs using the butterfly with W_4^0 and W_4^1. Finally the two 4-point results, E[k] and O[k], combine into the full 8-point DFT using the butterfly with W_8^0..W_8^3. This bottom-up order, applied stage by stage instead of recursive call by recursive call, is exactly the iterative FFT structure built in Section 11.
Radix-2 Decimation-in-Time FFT
Building the 8-Point FFT
19

## Slide 20
SECTION 10 · BIT-REVERSAL ORDERING
Why Bit-Reversal Appears in the Iterative Algorithm
The recursive decomposition tree keeps re-sorting samples by parity: even/odd, then even/odd of each half, then again.
If that same sorting is instead done once, up front, as a single index permutation, the rest of the algorithm becomes purely local: it only ever combines neighboring elements at each stage, in place.
That single permutation is bit-reversal: write the index in binary and reverse the order of its bits.
For N = 8, indices need 3 bits (log₂ 8 = 3):
Original index | Binary | Bits reversed | Bit-reversed index
0 | 000 | 000 | 0
1 | 001 | 100 | 4
2 | 010 | 010 | 2
3 | 011 | 110 | 6
4 | 100 | 001 | 1
5 | 101 | 101 | 5
6 | 110 | 011 | 3
7 | 111 | 111 | 7
Radix-2 Decimation-in-Time FFT
Bit-Reversal Ordering
20

## Slide 21
SECTION 10 · BIT-REVERSAL ORDERING
The Bit-Reversed Input Ordering for N = 8
Natural order (as stored / sampled)
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
↓ reorder using the bit-reversed index from the table on the previous slide
Bit-reversed order (as fed into the iterative FFT)
x[0]
x[4]
x[2]
x[6]
x[1]
x[5]
x[3]
x[7]
Two representations, one algorithm. The mathematical recursion in Section 9 sorts samples by repeatedly separating evens from odds; the iterative flow graph achieves an identical grouping by reading the input in bit-reversed order first, and then only ever combining adjacent pairs, then adjacent groups of four, then the final group of eight.
Notice that the bit-reversed order, x[0], x[4], x[2], x[6], x[1], x[5], x[3], x[7], is exactly the order the leaves appeared in the decomposition tree on the previous section's slide, read left to right. This is not a coincidence: bit-reversal is simply the flattened, iterative equivalent of the recursive even/odd splitting.
Radix-2 Decimation-in-Time FFT
Bit-Reversal Ordering
21

## Slide 22
SECTION 11 · BUILDING IN STAGES
The 8-Point FFT Organizes Into log₂(8) = 3 Stages
Number of stages = log2(N) = log2(8) = 3
Each stage corresponds to one level of the recursive decomposition tree, read bottom-up: combine 1-point results into 2-point results, combine 2-point results into 4-point results, combine 4-point results into the final 8-point result.
Stage | Combines | Butterfly size | Twiddle factors used | Number of butterflies
1 | 1-pt results → 2-pt results | N=2 | W₂⁰ = 1 (trivial) | 4
2 | 2-pt results → 4-pt results | N=4 | W₄⁰, W₄¹ | 4
3 | 4-pt results → 8-pt result | N=8 | W₈⁰, W₈¹, W₈², W₈³ | 4
Every stage has exactly N/2 = 4 butterflies. This is because every butterfly consumes 2 inputs and produces 2 outputs, and every stage processes all N = 8 data points exactly once. With N/2 butterflies per stage and log₂N = 3 stages, the total butterfly count is:
(N/2) × log₂N = 4 × 3 = 12 butterflies for the full 8-point transform. Sections 13 and 14 build on this count directly.
Radix-2 Decimation-in-Time FFT
FFT Stages
22

## Slide 23
SECTION 11 · BUILDING IN STAGES
Stage 1: Four 2-Point Butterflies
Inputs: the bit-reversed sequence, taken two samples at a time.
Butterfly | Inputs (bit-reversed order) | Twiddle | Output top = A+B | Output bottom = A−B
1 | x[0], x[4] | W₂⁰ = 1 | x[0]+x[4] | x[0]−x[4]
2 | x[2], x[6] | W₂⁰ = 1 | x[2]+x[6] | x[2]−x[6]
3 | x[1], x[5] | W₂⁰ = 1 | x[1]+x[5] | x[1]−x[5]
4 | x[3], x[7] | W₂⁰ = 1 | x[3]+x[7] | x[3]−x[7]
Every twiddle factor in Stage 1 is trivial. A 2-point DFT only ever needs W₂⁰ = 1, so no genuine complex multiplication happens anywhere in this stage, only additions and subtractions. Each butterfly consumes 2 adjacent samples from the bit-reversed array and writes its two outputs back to the same two positions (an “in-place” computation), which is exactly what makes the iterative, memory-efficient hardware implementation possible.
Butterflies in this stage: 4 (= N/2)
Radix-2 Decimation-in-Time FFT
Stage 1
23

## Slide 24
SECTION 11 · BUILDING IN STAGES
Stage 2: Combine Into Four-Point Results
Inputs: the four 2-point results from Stage 1, combined in groups of four using the 4-point twiddle factors.
Group | Butterfly | Stage-1 inputs used | Twiddle | Outputs
A | k=0 | (x0+x4), (x2+x6) | W₄⁰ = 1 | sum, difference
A | k=1 | (x0−x4), (x2−x6) | W₄¹ = −j | sum, difference (after −j rotation)
B | k=0 | (x1+x5), (x3+x7) | W₄⁰ = 1 | sum, difference
B | k=1 | (x1−x5), (x3−x7) | W₄¹ = −j | sum, difference (after −j rotation)
Group A produces E[0..3] (from even samples), Group B produces O[0..3] (from odd samples). W₄¹ = −j is another trivial twiddle factor: multiplying by −j swaps the real and imaginary parts and flips one sign, so it also needs no true multiplier (Section 17). Butterflies in this stage: 4 (= N/2).
Radix-2 Decimation-in-Time FFT
Stage 2
24

## Slide 25
SECTION 11 · BUILDING IN STAGES
Stage 3: Final Combination Into the 8-Point Result
Inputs: the two 4-point results, E[k] (Group A) and O[k] (Group B), combined with the full set of 8-point twiddle factors.
Butterfly (k) | Inputs | Twiddle W₈ᵏ | Output X[k] = E[k]+W₈ᵏO[k] | Output X[k+4] = E[k]−W₈ᵏO[k]
0 | E[0], O[0] | 1 | X[0] | X[4]
1 | E[1], O[1] | 0.7071−j0.7071 | X[1] | X[5]
2 | E[2], O[2] | −j | X[2] | X[6]
3 | E[3], O[3] | −0.7071−j0.7071 | X[3] | X[7]
This is exactly the equation pair from Section 6, evaluated four times. Only butterflies k=1 and k=3 require a genuine complex multiplication (by W₈¹ and W₈³); k=0 and k=2 use trivial twiddle factors (1 and −j). Butterflies in this stage: 4 (= N/2). After this stage, the outputs X[0] through X[7] are already in natural, non-permuted order, which is the DIT property noted in Section 5's comparison table.
Radix-2 Decimation-in-Time FFT
Stage 3
25

## Slide 26
SECTION 12 · NUMERICAL EXAMPLE
A Fully Worked 8-Point FFT: x[n] = 1, 2, ..., 8
Input sequence, natural order
x[0]=1
x[1]=2
x[2]=3
x[3]=4
x[4]=5
x[5]=6
x[6]=7
x[7]=8
Reordered by bit-reversal (Section 10), ready for the iterative stages
x[0]=1
x[4]=5
x[2]=3
x[6]=7
x[1]=2
x[5]=6
x[3]=4
x[7]=8
Plan for the next three slides. Starting from the bit-reversed sequence above, [1, 5, 3, 7, 2, 6, 4, 8], every butterfly in all three stages will be calculated explicitly: which two numbers go in (A and B), which twiddle factor is used, and what the sum (A+B) and difference (A−B) are. No step is skipped and no result is only stated.
At the end, the eight outputs X[0] ... X[7] will be checked against the direct DFT summation from Section 2, to confirm the FFT and DFT produce identical numbers.
Radix-2 Decimation-in-Time FFT
Numerical Example
26

## Slide 27
SECTION 12 · NUMERICAL EXAMPLE
Stage 1 Calculation: Four Trivial 2-Point Butterflies
Butterfly | A | B | Twiddle | A + B | A − B
1 (x0,x4) | 1 | 5 | 1 | 1+5 = 6 | 1−5 = −4
2 (x2,x6) | 3 | 7 | 1 | 3+7 = 10 | 3−7 = −4
3 (x1,x5) | 2 | 6 | 1 | 2+6 = 8 | 2−6 = −4
4 (x3,x7) | 4 | 8 | 1 | 4+8 = 12 | 4−8 = −4
Stage 1 outputs, in position order
6
-4
10
-4
8
-4
12
-4
All values here happen to be real because the twiddle factor is 1 in every Stage-1 butterfly (a 2-point DFT never needs a rotation). Complex values first appear in Stage 2, where W4^1 = −j is used.
Radix-2 Decimation-in-Time FFT
Numerical Example
27

## Slide 28
SECTION 12 · NUMERICAL EXAMPLE
Stage 2 Calculation: Combine Into Four-Point Results
Group | k | A | B | Twiddle W₄ᵏ | A + W₄ᵏB | A − W₄ᵏB
A | 0 | 6 | 10 | 1 | 6+10 = 16 | 6−10 = −4
A | 1 | −4 | −4 | −j | −4+(−j)(−4) = −4+4j | −4−(−j)(−4) = −4−4j
B | 0 | 8 | 12 | 1 | 8+12 = 20 | 8−12 = −4
B | 1 | −4 | −4 | −j | −4+(−j)(−4) = −4+4j | −4−(−j)(−4) = −4−4j
Stage 2 outputs (Group A = E[0..3], Group B = O[0..3])
E[0] | E[1] | E[2] | E[3] | O[0] | O[1] | O[2] | O[3]
16 | −4+4j | −4 | −4−4j | 20 | −4+4j | −4 | −4−4j
W4^1 = −j is a trivial rotation: multiplying by −j swaps real and imaginary parts and negates one of them, so (−j)(−4) = 4j needs only a sign flip and a swap, not a general complex multiplier (see Section 17).
Radix-2 Decimation-in-Time FFT
Numerical Example
28

## Slide 29
SECTION 12 · NUMERICAL EXAMPLE
Stage 3 Calculation: Final Combination Into X[k]
k | A = E[k] | B = O[k] | Twiddle W₈ᵏ | X[k] = A+W₈ᵏB | X[k+4] = A−W₈ᵏB
0 | 16 | 20 | 1 | 16+20 = 36 | 16−20 = −4
1 | −4+4j | −4+4j | 0.7071−0.7071j | −4+4j+j5.657 = −4+9.657j | −4+4j−j5.657 = −4−1.657j
2 | −4 | −4 | −j | −4+4j | −4−4j
3 | −4−4j | −4−4j | −0.7071−0.7071j | −4−4j+j5.657 = −4+1.657j | −4−4j−j5.657 = −4−9.657j
Note for k=1 and k=3: W₈ᵏ·B is computed as a full complex multiplication (Section 17), e.g. for k=1: (0.7071−0.7071j)(−4+4j) = 0 + j5.657. These are the only two genuine complex multiplications in the entire 8-point transform (see Section 14).
Final outputs X[0] .. X[7], natural order (no permutation needed for DIT)
X[0] | X[1] | X[2] | X[3] | X[4] | X[5] | X[6] | X[7]
36 | −4+9.657j | −4+4j | −4+1.657j | −4 | −4−1.657j | −4−4j | −4−9.657j
Radix-2 Decimation-in-Time FFT
Numerical Example
29

## Slide 30
SECTION 12 · NUMERICAL EXAMPLE
Verifying the FFT Result Against the Direct DFT
Cross-check 1: X[0] must equal the sum of all samples
X[0] = Σ x[n] = 1+2+3+4+5+6+7+8 = 36 matches the FFT result X[0] = 36
Cross-check 2: direct evaluation of X[1] from the DFT definition
X1 = Σn=07 x[n]·W₈n = −4 + j(4+4√2) = −4 + j9.657 matches the FFT result X[1] = −4+9.657j
Cross-check 3: conjugate symmetry (x[n] is real-valued)
Pair | Expected relation X[N−k] = X[k]* | FFT result
X[7] vs X[1] | conj(−4+9.657j) = −4−9.657j | X[7] = −4−9.657j ✓
X[6] vs X[2] | conj(−4+4j) = −4−4j | X[6] = −4−4j ✓
X[5] vs X[3] | conj(−4+1.657j) = −4−1.657j | X[5] = −4−1.657j ✓
X[4] | must be purely real (Nyquist bin) | X[4] = −4 ✓
Every check agrees. The 12-butterfly FFT computation and the 64-multiply direct DFT summation produce numerically identical results, as they must: the FFT is an algorithm for the DFT, not a different transform (Section 3).
Radix-2 Decimation-in-Time FFT
Numerical Example
30

## Slide 31
SECTION 13 · MATH ↔ FLOW GRAPH
How Every Equation Maps Onto the Flow Graph
DFT equation
X[k] = Σ x[n] W_N^(nk)
The full signal-flow graph, start to finish, computes this sum for every k.
Even/odd decomposition
n = 2r or n = 2r+1
The vertical position at which a sample first enters the graph (its row).
Smaller DFTs
E[k], O[k]
The sub-networks feeding each butterfly stage; recursively, more sub-networks feeding those.
Twiddle multiplication
W_N^k · O[k]
The single multiplier symbol (⊗) drawn on the lower input wire of every butterfly.
Butterfly
X[k]=A+B, X[k+N/2]=A−B
The crossing pair of wires plus the (+) and (−) nodes.
Recursive decomposition
tree of N/2, N/4, ... point DFTs
The number of columns (stages) in the graph, and which wires cross where.
FFT stages
log₂N columns of butterflies
Each vertical column of the flow graph, left to right.
Final samples
X[0] ... X[N−1]
The right-hand edge of the graph, in natural order for DIT.
Radix-2 Decimation-in-Time FFT
Math to Flow Graph
31

## Slide 32
SECTION 14 · OPERATION COUNT
Deriving the Number of Multiplications and Additions
Number of stages: log₂N (Section 11).
Butterflies per stage: N/2 (every stage touches all N samples in groups of 2).
Total butterflies: (N/2)×log₂N.
Total butterflies = (N/2) log2N
Each butterfly performs, in the generic case:
Operation | Count per butterfly
Complex multiplication (forming B = W_N^k · O[k]) | 1
Complex addition (A + B) | 1
Complex subtraction (A − B) | 1 (2 real add/sub operations total)
Multiplying out across all butterflies: complex multiplications = (N/2) log₂N. Complex additions/subtractions = 2 × (N/2) log₂N = N log₂N.
Radix-2 Decimation-in-Time FFT
Operation Count
32

## Slide 33
SECTION 14 · OPERATION COUNT
Operation Count for N = 8, and Trivial-Twiddle Savings
Quantity | Formula | N = 8 value
Stages | log₂N | 3
Butterflies per stage | N/2 | 4
Total butterflies | (N/2) log₂N | 12
Complex multiplications (generic case) | (N/2) log₂N | 12
Complex additions/subtractions | N log₂N | 24
But some twiddle factors are trivial
W_N^k = 1, −1, j, or −j needs no general complex multiplier: only sign flips and/or a swap of real/imaginary parts (Section 17).
In the worked example (Section 12): Stage 1 uses only W₂^0=1 (4 trivial butterflies). Stage 2 uses only W₄^0=1 and W₄^1=−j (4 trivial butterflies). Stage 3 uses W₈^0=1 and W₈^2=−j (trivial) plus W₈^1 and W₈^3 (genuine).
Result: of the 12 “generic” complex multiplications counted above, only 2 are genuine general complex multiplications for N = 8 (both in Stage 3, k=1 and k=3). The other 10 reduce to sign flips and swaps. This is why real FFT implementations special-case trivial twiddle factors instead of running every butterfly through a full multiplier.
Radix-2 Decimation-in-Time FFT
Operation Count
33

## Slide 34
SECTION 15 · DIT FFT DATA FLOW
Complete 8-Point Radix-2 DIT Flow Graph
x[0]=1
x[4]=5
x[2]=3
x[6]=7
x[1]=2
x[5]=6
x[3]=4
x[7]=8
1
1
1
1
1
-j
1
-j
1
W8^1
-j
W8^3
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
Bit-reversed input
Stage 1
Stage 2
Stage 3
Output (natural order)
Data flows left to right. Each crossing pair is one butterfly; the boxed label is its twiddle factor. Twiddle span doubles each stage (1, 2, then 4 rows apart), matching the recursive decomposition of Section 9.
Radix-2 Decimation-in-Time FFT
DIT FFT Data Flow
34

## Slide 35
SECTION 16 · DIT VS. DIF
Decimation-in-Time vs. Decimation-in-Frequency, Revisited
Having derived and fully calculated the DIT algorithm, it is worth restating precisely how its dual, DIF, differs, now that every term in the table below has been defined and worked through an example.
Feature | Radix-2 DIT | Radix-2 DIF
Decomposition domain | Time / input sequence | Frequency / output sequence
Input ordering | Bit-reversed | Natural
Output ordering | Natural | Bit-reversed
First operation | Small-DFT decomposition, then combine (butterfly at the end of each merge) | Butterfly first (add/sub), then twiddle, then recurse into smaller DFTs
Twiddle placement in the butterfly | Before the add/subtract (multiply, then combine) | After the add/subtract (combine, then multiply)
Typical interpretation | “Split input samples, then combine into the spectrum” | “Split frequency outputs, then simplify”
Both algorithms compute the identical DFT and both require exactly (N/2)log₂N butterflies. Choosing between them in practice is usually a matter of which ordering (input or output) is more convenient for the surrounding system, not computational cost.
Radix-2 Decimation-in-Time FFT
DIT vs DIF
35

## Slide 36
SECTION 17 · COMPLEX ARITHMETIC
The Complex Multiplication Inside Every Butterfly
General complex multiplication
(a+jb)(c+jd) = (ac−bd) + j(ad+bc)
4 real multiplications (ac, bd, ad, bc) and 2 real additions/subtractions.
Applied to B = W_N^k · O[k]: a,b are the real/imaginary parts of W_N^k; c,d are the real/imaginary parts of O[k].
A real adder costs far less silicon/logic and less latency than a real multiplier, so the multiply count, not the add count, usually dominates FFT hardware cost.
Special case: multiplying by j
j(a+jb) = ja + j2b = −b + ja
Multiplying by j (or −j) only swaps the real and imaginary parts and flips one sign; multiplying by −1 only flips both signs.
No real multiplier is needed at all, just wiring and a sign inversion.
This is exactly why the trivial twiddle factors identified in Sections 8 and 14 (1, −1, j, −j) can be special-cased out of the multiply count in hardware.
Hardware connection: an FPGA/ASIC butterfly processing element typically implements the general complex multiplier as 3 or 4 real multiplier blocks (3 with the Karatsuba-style trick that trades a multiply for extra adds) plus adders, but recognizes trivial twiddle factors in the control logic and bypasses the multiplier entirely for them (Section 18).
Radix-2 Decimation-in-Time FFT
Complex Arithmetic
36

## Slide 37
SECTION 18 · HARDWARE MAPPING
From Algorithm to RTL: FFT Hardware Building Blocks
Complex multipliers
  Implement B = W_N^k · O[k]; often the most area/power-costly block, so trivial twiddles bypass them.
Complex adders
  Form A+B and A−B; cheap, and needed twice as often as multipliers (Section 14).
Registers / delay lines
  Hold intermediate butterfly outputs between stages in pipelined or streaming designs.
Memory (input/working RAM)
  Stores samples between stages; in-place butterfly computation (Section 11) minimizes memory needed.
Address generation / bit-reversal unit
  Produces the bit-reversed read/write addresses of Section 10, often as a small counter with reversed bit wiring.
Twiddle-factor ROM
  Stores precomputed W_N^k values (Section 8); symmetry (Section 8) allows storing only a quarter-circle.
Streaming vs. burst architectures
Burst (memory-based): one butterfly processing element reused for all stages; slower but small area.
Streaming (pipelined): one processing element per stage, data flows continuously; fast, more area.
Conceptual hardware datapath
Input Memory
↓
Bit-Reversal / Address Generation
↓
Butterfly Processing Element
↓
Twiddle ROM + Complex Multiplier
↓
Butterfly Processing Element (next stage)
↓
FFT Output
This deck stays at the conceptual RTL-mapping level; vendor-specific FFT IP cores add configuration for streaming width, radix mixing, and scaling, on top of the same underlying algorithm.
Radix-2 Decimation-in-Time FFT
Hardware Mapping
37

## Slide 38
SECTION 19 · FIXED-POINT IMPLEMENTATION
Why Fixed-Point Arithmetic Needs Care in FFT Hardware
FPGA and ASIC FFT implementations very often use fixed-point (integer with an implied binary point) rather than floating-point arithmetic, because fixed-point multipliers and adders are smaller, faster, and lower power. This efficiency comes with bookkeeping responsibilities:
Concern | What it means here
Quantization | Representing real/imaginary parts and twiddle factors with a finite number of bits introduces small rounding errors.
Dynamic range | Signal magnitudes can grow through the stages; the word length must cover the largest value that can occur.
Bit growth | Each complex addition can grow the required word length by up to 1 bit (see example below).
Overflow | If the word length is not grown or scaled, sums can wrap around and corrupt the result.
Rounding / saturation | After multiplication, results must be rounded or truncated back to a fixed word length; saturation clips instead of wrapping on overflow.
A minimal bit-growth example
a, b ∈ [−8,7] (4-bit signed) → a+b ∈ [−16,14] (needs 5 bits)
Every butterfly addition can add 1 bit of headroom in the worst case. Across log₂N = 3 stages for N=8, up to 3 extra guard bits may be needed if no scaling is applied between stages.
Scaling strategies
Block scaling: scale the whole data block once, before or after the transform.
Stage scaling: divide by 2 (a free right-shift) after every stage to bound growth.
Saturation: clip rather than wrap on overflow, trading a bounded error for guaranteed stability.
Guard bits: carry a few extra fractional/integer bits through the pipeline and truncate only at the end.
Radix-2 Decimation-in-Time FFT
Fixed-Point Implementation
38

## Slide 39
SECTION 20 · TROUBLESHOOTING
Common Mistakes When Implementing Radix-2 DIT
Confusing DIT with DIF
Applying bit-reversal to the wrong side (output instead of input), or placing the twiddle multiply after the add/sub instead of before.
Wrong sign in the twiddle factor
Using e^(+j2π/N) instead of e^(−j2π/N) inverts the transform direction (DFT vs. inverse DFT).
Wrong bit-reversal order
Reversing bits across the wrong word length (e.g. reversing 4 bits for an 8-point, 3-bit transform) scrambles the input mapping.
Using W_N instead of W_(N/2) at the wrong stage
Each stage's twiddle factors come from the DFT size active at that stage (Section 6); reusing the top-level W_N everywhere gives incorrect phase rotations.
Incorrect butterfly pairing
Combining the wrong two elements (e.g. adjacent array elements instead of elements separated by the correct stage span) breaks the whole recursion (see Section 15's span pattern: 1, 2, 4).
Mixing natural and bit-reversed ordering
Reading inputs in natural order but writing outputs as if bit-reversed (or vice-versa) silently permutes the spectrum.
Forgetting complex arithmetic
Treating W_N^k · O[k] as a real multiplication drops the imaginary cross-terms (Section 17).
Incorrect FFT normalization
The DFT/FFT pair defined here has no 1/N factor; forgetting or double-applying a 1/N (usually needed only on the inverse transform) scales results incorrectly.
Confusing bin index with physical frequency
X[k] is a bin index, not a frequency in Hz; the actual frequency is k·f_s/N, and bins above N/2 represent negative frequencies for real input.
Radix-2 Decimation-in-Time FFT
Troubleshooting
39

## Slide 40
SECTION 22 · SUMMARY
Final Mental Model
Final Mental Model
SECTION 22 · SUMMARY
N-point DFT
↓
Split time samples
↓
Even + Odd
↓
Two N/2-point DFTs
↓
Twiddle factor
↓
Butterfly
↓
Repeat recursively
↓
log₂N stages
↓
FFT
Key equations to remember
W_N = e^(-j2π/N)
X[k] = E[k] + W_N^k O[k]
X[k+N/2] = E[k] − W_N^k O[k]
Stages = log₂N
Butterflies = (N/2)log₂N
Radix-2 Decimation-in-Time FFT
Summary
42

## Slide 41
REFERENCES
Sources for Further Study
A. V. Oppenheim and R. W. Schafer
Discrete-Time Signal Processing
The standard graduate reference for the DFT, the radix-2 FFT derivation, and decimation-in-time / decimation-in-frequency structures.
J. G. Proakis and D. G. Manolakis
Digital Signal Processing: Principles, Algorithms, and Applications
Detailed treatment of FFT algorithms, operation counts, and fixed-point implementation issues.
MathWorks
MATLAB Documentation: fft, bitrevorder
Reference documentation for the built-in FFT function and bit-reversal ordering utility used in Section 21.
Cooley, J. W. and Tukey, J. W. (1965)
“An Algorithm for the Machine Calculation of Complex Fourier Series,” Mathematics of Computation
The original paper describing the fast Fourier transform algorithm underlying this derivation.
This deck is a self-contained study notebook. Revisit Sections 6-15 for the full derivation-to-implementation chain whenever implementing an FFT in MATLAB, FPGA, or RTL.
Radix-2 Decimation-in-Time FFT
References
43